## Slide 1: Simulation and Debug
Dr. Ruba Alkhasawneh

## Slide 2: Why Simulation?
Advantages:
  Cost-effective: reduce development costs as it eliminates the need for physical hardware prototypes.
  Early error detection: provide early bug detection before the design is implemented on the hardware.
  High visibility of all signals in the design.
  Faster time-to-market: provides early detection of design issues which reduces the overall development time.
Disadvantages:
  Hardware testing & performance: e.g. interacting with external peripherals and sensors.
  Can take a long time to run – Software-based.

## Slide 3: Testbench
A test bench or testing workbench is an environment used to verify the correctness or soundness of a design or model.

## Slide 4: Verilog Testbench
Source: https://fpgacademy.org

## Slide 5: Handy Verilog Testbench Constructs
$dumpfile(“testbench_results.vcd”);
Specifies file to dump signals to view later in a waveform viewer
$dumpvars;
Dump all signals to dumpfile
$display("\t\ttime,\tclk,\treset,\tenable,\tcount");
Write text to console once
$monitor("%d,\t%b,\t%b,\t%b,\t%d",$time, clk,reset,enable,count);
Monitor signal activity – write upon events of sensitivity list
Source: https://fpgacademy.org

## Slide 6: Mentor ModelSim Overview
ModelSim is a multi-language HDL (Verilog/VHDL) simulation environment. It can be used independently or Intel Quartus can create startup scripts and link designs to ModelSim.
Intel Quartus has a license to distribute Modelsim-Altera with Quartus.

## Slide 7: Modelsim setup - 1
Go to Tools  Options  EDA Tool Options. In ModelSim-Altera, enter the executable pathway.
This path might be different for your own installation!

## Slide 8: Setting up ModelSim from Intel Quartus
Assignments  Settings EDA Tools Settings  Simulation
In NativeLink Settings  Test Benches  NEW
Add New testbench  OK

## Slide 9: ModelSim GUI
Launching ModelSim from Quartus Tools Run Simulation Tool  RTL Simulation
Command Transcript Window
Testbench File
Simulation Objects